## Slide 1: On the Accuracy of Tor Bandwidth Estimation
Rob Jansen and Aaron Johnson
U.S. Naval Research Laboratory
  Rob Jansen
Center for High Assurance Computer Systems
U.S. Naval Research Laboratory
Passive and Active Measurement Conference 2021
Virtual Event
March 29th – 31st , 2021

## Slide 2: Main Results
  Tor underestimates its total network bandwidth capacity by about 200 Gbit/s (50%)
    ~20% of relays have > 50% variation in bandwidth estimates
  We discovered significant error in bandwidth capacity estimation, with larger error for:
    High-capacity relays
    Exit relays
    Relays with lower uptimes
  Inaccurate capacity measurements may lead to suboptimal load balancing
    Affects performance for all Tor users
200 Gbit/s (50%)

## Slide 3: Main Contributions
  Analysis of passive relay measurements
    Understand variation in capacity estimates from historical data
    Variation indicates inaccurate estimation
  Active speed test experiment to measure relays
    Flood relays with traffic to drive up their observed bandwidth
    Cause relays to learn their bandwidth limits and better estimate their capacity
    Analyze change in bandwidth reports before/after speed test

## Slide 4: Main Contributions
  Analysis of passive relay measurements
    Understand variation in capacity estimates from historical data
    Variation indicates inaccurate estimation
  Active speed test experiment to measure relays
    Flood relays with traffic to drive up their observed bandwidth
    Cause relays to learn their bandwidth limits and better estimate their capacity
    Analyze change in bandwidth reports before/after speed test

## Slide 5: Definitions and Problem
  Fowarding capacity (i.e., the true capacity)
    The max sustainable rate at which a relay can forward traffic
    This value is unknown, so relays must estimate it
  Observed bandwidth
    The max throughput a relay has sustained for any 10 second period over last 5 days
    This value is reported to Tor metrics every 18 hours
    Load balancing weights are derived from observed bandwidth
  Problem: observed bandwidth != forwarding capacity
    Insufficient client traffic limits the observed bandwidth
    Underutilized relay will never learn its true forwarding capacity
    Weighting based on observed bandwidth will be inaccurate

## Slide 6: Definitions and Problem
  Fowarding capacity (i.e., the true capacity)
    The max sustainable rate at which a relay can forward traffic
    This value is unknown, so relays must estimate it
  Observed bandwidth
    The max throughput a relay has sustained for any 10 second period over last 5 days
    This value is reported to Tor metrics every 18 hours
    Load balancing weights are derived from observed bandwidth
  Problem: observed bandwidth != forwarding capacity
    Insufficient client traffic limits the observed bandwidth
    Underutilized relay will never learn its true forwarding capacity
    Weighting based on observed bandwidth will be inaccurate

## Slide 7: Definitions and Problem
  Fowarding capacity (i.e., the true capacity)
    The max sustainable rate at which a relay can forward traffic
    This value is unknown, so relays must estimate it
  Observed bandwidth
    The max throughput a relay has sustained for any 10 second period over last 5 days
    This value is reported to Tor metrics every 18 hours
    Load balancing weights are derived from observed bandwidth
  Problem: observed bandwidth != forwarding capacity
    Insufficient client traffic limits the observed bandwidth
    Underutilized relay will never learn its true forwarding capacity
    Weighting based on observed bandwidth will be inaccurate

## Slide 8: Active Speed Test Experiment
  Hypothesis: the predominant error is to underestimate the true capacity of Tor relays
  Experiment: perform a speed test on the live Tor network
    Actively attempt to send 1 Gbit/s of traffic through each relay
    Extra traffic should increase relays’ observed bandwidth
    New observed bandwidths should better reflect forwarding capacity of relay

## Slide 9: Speed Test Experiment
Relay being tested
Experiment Machine (1 Gbit/s)
Return ‘echo’ cells without decrypting
Send ‘echo’ cells
Forward encrypted cells like normal
10 TCP connections
10 TCP connections

## Slide 10: Speed Test Results
Tor underestimates its total capacity by about 50%

## Slide 11: Speed Test Results
The estimated capacity increased after our experiment for most relays (some by a 10x or greater factor)

## Slide 12: Speed Test Results
We discovered more capacity on higher-capacity relays

## Slide 13: Speed Test Results
Load balancing weights changed significantly for many relays (some by a 10x or greater factor)

## Slide 14: Summary
  Contributions
    Historical measurements: ~20% of relays have >50% variation in bandwidth estimates
    Active speed test experiment:
      Tor underestimates total capacity by ~50%
      Larger error associated with high-capacity, exit, and lower uptime relays
  Research artifacts available at:
    https://torbwest-pam2021.github.io
  Contact
    <rob.g.jansen@nrl.navy.mil>, robgjansen.com, @robgjansen

## Slide 15: Analysis of Historical Bandwidth Data
  Use relative standard deviation to understand variation
    A(r,w) = adv. bws for relay r during week w
    RSD(A(r,w)) = stdev(A(r,w)) / mean(A(r,w))
  We find significant variation in relays’ bandwidths
    the capacity estimates of 25% of relays vary by 41% or more
    the capacity estimates of 10% of relays vary by 71% or more
    some relays’ capacity estimates vary by more than 200%

## Slide 16: Speed Test Results
We discovered more capacity on lower-uptime relays