## Slide 1: Co-opting Linux Processes for High-Performance Network Simulation
Rob Jansen, U.S. Naval Research Laboratory
Jim Newsome, Tor Project
Ryan Wails, Georgetown University & U.S. Naval Research Laboratory
  Rob Jansen, Ph.D.
  Computer Security Research Scientist
Center for High Assurance Computer Systems
U.S. Naval Research Laboratory
USENIX Annual Technical Conference Carlsbad, CA, USA
July 11th, 2022
USENIX ATC’22 Best Paper Award!

## Slide 2: Main Takeaways
Runtime (s)
Designed a new, hybrid network simulator/emulator
    co-opts Linux processes into a discrete-event network simulation that emulates kernel functionality
    enables large-scale, distributed system experiments
    Merged into the open-source Shadow project and synonymous with Shadow v2
    Artifacts: https://netsim-atc2022.github.io
Read the paper!
shadow.github.io
2.3x faster than Shadow v1
3.4x faster than NS-3
43x faster than gRaIL [ToN’19]

## Slide 3: Outline
motivation
design
evaluation

## Slide 4: Requirements for Large Distributed System Experimentation
Important properties of test networks:
    Controllable: isolate important factors
    Replicable: identically replicate experiments (determinism)
Requirements for large distributed systems:
    Accurate: directly execute system software (not an abstraction)
    Scalable: decouple from time, computational constraints of host
Controllable
Accurate
Scalable
Replicable
Our approach
Notes:   Controllable:
    Prevent confounding influence, cascading network effects
  Replicable:
    Enables results to be independently verified
  Accurate:
    Reproduce complex application-layer logic with high fidelity
  Scalable:
    Prevents over-provisioning and time-distortion
    Enables larger scales (may run faster or slower than real time)
    More confidence in results with fewer trials

## Slide 5: Problems with Traditional Approaches
Simulation (e.g., ns-3)
    Not realistic: runs abstractions instead of real applications
    Hard to maintain and can lead to invalid results
Emulation (e.g., mininet)
    Not controllable: results will not be identical
    Not scalable: CPU overload  time distortion
Mininet
> sudo mn

## Slide 6: Problems with Traditional Approaches
Simulation (e.g., ns-3)
    Not realistic: runs abstractions instead of real applications
    Hard to maintain and can lead to invalid results
Emulation (e.g., mininet)
    Not controllable: results will not be identical
    Not scalable: CPU overload  time distortion
Mininet
> sudo mn
CPU overload with >20 hosts
Forwarding capacity limited: fewer packets than expected are forwarded

## Slide 7: Hybrid Architectures and Challenges
Hybrid architecture
    Network simulation, but directly execute application code
    Enjoys advantages of both simulation and emulation
    Best opportunity to scale to large-scale distributed systems
Architecture | Example Tool | Scalability | Realism | Control
Emulation | Mininet |  |  | 
Simulation | NS-3 |  |  | 
Hybrid | This work |  |  | 
Notes: scalability: Experiments scale independent of CPU constraints
realism: Unmodified apps can be directly run without rebuilding
control: Results can be deterministically replicated

## Slide 8: Limitations of Hybrid Architectures (1)
Executing application code via plugin (link-map) namespaces
    appid = dlmopen(app.so)
    func = dlsym(appid, “main”)
    func()
NS-3-DCE, Shadow
Limitations
    Compatibility (must build PIC/PIE)
    Correctness (intercept libcalls only)
    Maintainability (custom ld, threading)

## Slide 9: Limitations of Hybrid Architectures (1)
Executing application code via plugin (link-map) namespaces
    appid = dlmopen(app.so)
    func = dlsym(appid, “main”)
    func()
NS-3-DCE, Shadow
Limitations
    Compatibility (must build PIC/PIE)
    Correctness (intercept libcalls only)
    Maintainability (custom ld, threading)

## Slide 10: Limitations of Hybrid Architectures (2)
Executing code via Linux processes
    fork() + exec()  ptrace()
gRaIL [ToN’19]
Limitations: ptrace is slow!
    Process control: overhead quadratic in total number of processes
    Syscall interception: 4 context switches for every syscall
    Data transfer: extra syscall + mode change for every word of memory
Runtime (s)
gRaIL (on ns-3) is 13x slower than ns-3 alone

## Slide 11: Our Research Challenge
Can we design a tool with the performance benefits of a uni-process plugin-based architecture AND the improved modularity and isolation of a mutli-process architecture?

## Slide 12: Our Research Challenge

## Slide 13: Outline
motivation
design
evaluation

## Slide 14: Design Overview
Discrete-event packet-level network simulator
Directly executes apps as standard Linux processes
Intercepts all system calls made by apps and emulates them
Simulates system call behavior and networking
    File descriptors (files, sockets, pipes)
    Event notification (poll, epoll, select)
    Networking (buffers, protocols, ifaces)
    DNS and routing (latency, bandwidth)
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity

## Slide 15: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
Goal: efficiently parallelize simulation workload
Physical processors

## Slide 16: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
Goal: efficiently parallelize simulation workload
Physical processors
Virtual hosts and processes

## Slide 17: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
Goal: efficiently parallelize simulation workload
How many worker threads should we run?
Physical processors
Virtual hosts and processes

## Slide 18: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
Goal: efficiently parallelize simulation workload
How many worker threads should we run?

## Slide 19: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
Goal: efficiently parallelize simulation workload
Physical processors
Virtual hosts and processes
One thread per host!

## Slide 20: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
LP
LP
LP
LP
Goal: efficiently parallelize simulation workload
Physical processors
Logical processors (avoid CPU oversubscription)
Virtual hosts and processes
One thread per host

## Slide 21: Parallel Worker Threads
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
CPU
CPU
CPU
CPU
LP
LP
LP
LP
Goal: efficiently parallelize simulation workload
Physical processors
Logical processors (avoid CPU oversubscription)
Virtual hosts and processes
One thread per host
Thread scheduling:
    Work stealing
    Each LP starts a thread
      Runs all assigned events in current round (1 ms)
      Set thread to waiting
      Starts next waiting thread (if any)
    When all threads waiting
      Advance round clock
      Repeat

## Slide 22: Direct Execution
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Linux Kernel, Devices, Network
Sim Controller Process

## Slide 23: Direct Execution
App Process
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Sim Controller Process
LD_PRELOAD=shim.so
IPC=“ipc.shm”
vfork() + execvpe()
Injected shim.so library
Linux Kernel, Devices, Network

## Slide 24: Direct Execution
App Process
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Sim Controller Process
Injected shim.so library
Attach to “ipc.shm” for IPC
IPC
Linux Kernel, Devices, Network

## Slide 25: Direct Execution
App Process
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Sim Controller Process
Injected shim.so library
App is running and can communicate with controller
IPC
Linux Kernel, Devices, Network

## Slide 26: Syscall Interposition
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
…
Library N
Linked libraries
Controller Libraries
Linked libraries
Lib 0
Controller Code
Linux Kernel, Devices, Network

## Slide 27: Syscall Interposition
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
…
Library N
Controller Libraries
Lib 0
Controller Code
Linux Kernel, Devices, Network
1. Intercept libcalls (LD_PRELOAD)

## Slide 28: Syscall Interposition
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
…
Library N
Controller Libraries
Lib 0
Controller Code
Linux Kernel, Devices, Network
2. Intercept syscalls (seccomp)
1. Intercept libcalls (LD_PRELOAD)

## Slide 29: Syscall Interposition
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
…
Library N
Controller Libraries
Lib 0
Controller Code
Linux Kernel, Devices, Network
1. Intercept libcalls (LD_PRELOAD)
2. Intercept syscalls (seccomp)

## Slide 30: Syscall Interposition
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
…
Library N
Controller Libraries
Lib 0
Controller Code
Linux Kernel, Devices, Network
1. Intercept libcalls (LD_PRELOAD)
2. Intercept syscalls (seccomp)

## Slide 31: Syscall Emulation
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
Lib 0
Linux Kernel, Devices, Network
…
Library N
Controller Libraries
Controller Code
IPC
    File descriptors (files, sockets, pipes)
    Event notification (poll, epoll, select)
    Networking (buffers, protocols, ifaces)
    DNS and routing (latency, bandwidth)

## Slide 32: Syscall Emulation
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
Lib 0
Linux Kernel, Devices, Network
…
Library N
Controller Libraries
Controller Code
IPC
Emulate in Shim
faster
for hotpath syscalls (time)
    File descriptors (files, sockets, pipes)
    Event notification (poll, epoll, select)
    Networking (buffers, protocols, ifaces)
    DNS and routing (latency, bandwidth)

## Slide 33: Syscall Emulation
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Linux Kernel Syscall API
Injected shim.so library
Application Code
Library 1 (e.g. libc)
Lib 0
Linux Kernel, Devices, Network
Emulate in Shim
faster
for hotpath syscalls (time)
…
Library N
Controller Libraries
Controller Code
Emulate in Controller
slower (IPC overhead)
IPC: syscall args/data
IPC
    File descriptors (files, sockets, pipes)
    Event notification (poll, epoll, select)
    Networking (buffers, protocols, ifaces)
    DNS and routing (latency, bandwidth)

## Slide 34: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
IPC

## Slide 35: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory

## Slide 36: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
Shared memory + semaphores is the fastest IPC method for two processes running on
the same core

## Slide 37: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
1. Fixed-size control block
semaphores
syscall registers
simulation time

## Slide 38: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
1. Fixed-size control block
semaphores
syscall registers
simulation time
app stack
app heap
2. remap app memory to directly read/write data buffers

## Slide 39: Inter-Process Communication
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
1. Fixed-size control block
semaphores
syscall registers
simulation time
2. remap app memory to directly read/write data buffers
app stack
app heap

## Slide 40: Process Control
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
semaphores
syscall registers
simulation time
app stack
app heap

## Slide 41: Process Control
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
semaphores
syscall registers
simulation time
Write syscall registers
Signal controller semaphore
Wait on app semaphore
app stack
app heap

## Slide 42: Process Control
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
semaphores
syscall registers
simulation time
Write syscall registers
Signal controller semaphore
Wait on app semaphore
Read syscall registers
Return if nonblocking else leave app idle and return when ready
Signal app semaphore
Wait on controller semaphore
app stack
app heap

## Slide 43: Process Control
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
semaphores
syscall registers
simulation time
Properties:
    Controller worker thread and its app process run synchronously
    Ensures nonconcurrent access to app stack and heap memory
Write syscall registers
Signal controller semaphore
Wait on app semaphore
Read syscall registers
Return if nonblocking else leave app idle and return when ready
Signal app semaphore
Wait on controller semaphore
app stack
app heap

## Slide 44: Process Control
parallel workers
direct execution
syscall interposition
syscall emulation
IPC
process control
CPU affinity
Sim Controller Process
Injected shim.so library
App Process
shared memory
Use CPU pinning to pin each worker thread and all of its managed processes to the same core

## Slide 45: Outline
motivation
design
evaluation

## Slide 46: Evaluation: Large P2P Benchmarks
Faster and more scalable than the uni-process, plugin architecture!
Uses significantly less memory than the uni-process, plugin architecture!

## Slide 47: Evaluation: Large Tor Networks
Performance comparable to the state of the art for large Tor networks
Uses significantly less memory than the uni-process, plugin architecture!

## Slide 48: Main Takeaways
Runtime (s)
Designed a new, hybrid network simulator/emulator
    co-opts Linux processes into a discrete-event network simulation that emulates kernel functionality
    enables large-scale, distributed system experiments
    Merged into the open-source Shadow project and synonymous with Shadow v2
    Artifacts: https://netsim-atc2022.github.io
Read the paper!
shadow.github.io
2.3x faster than Shadow v1
3.4x faster than NS-3
43x faster than gRaIL [ToN’19]